## Slide 1: Sustainability Analysis of a Pedestrian Bridge made from Repurposed Wind Turbine Blades
Angela Nagle
University College Cork, Ireland
27 August, 2020

## Slide 2: Wind Turbine Blade Waste Problem in Ireland
Blades are Glass Fibre Reinforced Polymer (GFRP)
GFRP is difficult to recycle!
Turbines have 20 expected lifespan*
12-15 tonnes of GFRP material per MW of power (Jensen and Skelton, 2018)
By 2038, 2323 turbines expected to be decommissioned in Ireland
(estimated 64,800 tonnes of GFRP waste)
* Some wind farms are extending life up to 25-30 years, but this simply pushes waste problem out 5-10 years

## Slide 3: Current EoL Options for Blade Waste
Baseline Disposal Scenario: Cement co-processing is the most sustainable technology currently in high volume production (Nagle et al, 2020)
Pyrolysis & Mechanical Grinding are not economically viable for GFRP (WindEurope, 2020)
Environmental gains are made by using blade waste to substitute fuel and clinker raw material in cement co-processing

## Slide 4: Re-Wind Project
Sustainable Repurposing of Composite Wind Turbine Blade Waste
Expected Outcome: Viable businesses models for Wind Blade Repurposing that are sustainable.
https://www.re-wind.info/

## Slide 5: Pedestrian Blade Bridge Design
Short span pedestrian bridge designed using the lower section of two decommissioned turbine blades
Excellent Irish Opportunity Exists!
2020 Irish Program for Government: €1 million/day on cycle & walking infrastructure
EU Public Procurement for a Circular Economy encourages sourcing repurposed material
(Suhail et al, 2019)

## Slide 6: LCA Boundary Setting & Assumptions
Functional Unit: Disposition of 4500 kg blade waste over 60 years (Cradle to Grave)
Blades cut, then transported across Ireland for remanufacturing
Lower 2/3 blade replaces steel girders
Top 1/3 blade sent to landfill
Blades coated in epoxy protective layer
EoL Plan: Co-processing of GFRP girders, recycling of hardware
Wooden decking material, abutments, and maintenance schedule assumed equal to blade made with steel girders

## Slide 7: LCA Data (1): Comparison of the Impact of the Baseline v. Repurposing as Bridge Girders
Co-processing is compared to the substitution of the steel girders + co-processing at EoL

## Slide 8: LCA Data (2): Impact of the Full Bridge Assembly
The full bridge assembly has more impact than the benefits gained in replacing the steel girders with blade waste

## Slide 9: LCA Data (3): Process Impacts of Full Bridge Assembly

## Slide 10: Discussion of Actual Impacts
Repurposing of wind turbine blades as girders for pedestrian bridges is environmentally better than the baseline disposal method of co-processing in a cement kiln.
However, the positive impacts of this project are more likely in the awareness raising of ‘developing projects that can inspire and showcase the potential of a circular economy’. Ellen Macarthur says: Setting up exemplar projects in strategic places in the city can be an inspiring way to demonstrate what is practically possible... (Ellen Macarthur Foundation, 2019)

## Slide 11: Future Plans
Blade Bridge Project Status: Re-Wind is working with Cork County Council to design short span (8–15m) cattle and road flyover bridges along a new 23km cycleway. Limiting factor at the moment is sourcing blade waste!
Future Research Plans: Complete a Future Scenario Assessment and LCSA! Use the Sustainable Development Goals to select/create social indicators for the LCSA. Estimate GFRP recycling scenarios for 2080 in order to run consequential LCA on future GFRP disposal options.

## Slide 12: Thank You!!
AngelaJaneNagle@umail.ucc.ie